## Slide 1
IPEPG Features
Overseas Product Planning Dept.

## Slide 2
Geo coverage
  Must have: FR, DE, ES, IT, NO, SE, DK, FI, PL, BE, NL, CH, AT
  Good to gave: LT, LV, EE, CZ, SK, HU, PT, RU, UA, UK, IE
TV application
  General requirement
    Support multi-language (EU 27 languages)
    Push advertisement by Country & brands
    Support different skinning by multi brands
    Good UX – clear UI flow, menu tree not too deep, low latency, enable/disable IPEPG
    TCL customize Recommendation list - Later
  DTV EPG
    Enter IPEPG by GUIDE key or Smart portal
    Up to 21 days DTV EPG (show by Grid), can switch by page & whole day
    Channel list/order sync with local DTV channel
    Detail description, progress bar, poster, cast/crew, List of channels with same program
    cast/crew list link to show related TV/VOD list
    Jump to play TV program
    PVR
    List of channels with same program
    Related content & Recommendation
    Search
    Bookmark & Notification
    history

IP EPG Requirement - Basic

## Slide 3
TV specific requirements
  TV upload user habit of DTV system to server to do accurate recommendation
  sync with tablet and Phone
2nd Screen Support
  with single license bind to TV
  Sync EPG with TV
  tablet and Phone (IOS, android)
  User action push to TV
IP EPG requirement - Enhanced

## Slide 4
TV only
  1.TV is not connected to Internet
    User press GUIDE on RCU -> DVB SI EPG is displayed on the screen
  2.TV is connected to Internet
  User press GUIDE on RCU -> IP EPG CE-HTML or HTML5 application using browser engine is displayed on the screen
TV & nscreen with EPG application
  1.TV is connected to Internet
    User press GUIDE on RCU -> IP EPG CE-HTML or HTML5 application using browser engine is displayed on the screen & sync with nscreen
    Tablet/Phone connected to TV, then get metadata from TV and browse/play EPG on second screen.
DTV EPG scenario